## Slide 1
DSP Midterm, Group 03
Speech and silence
segmentation
Võ Thanh Quân: Binary Search
Vương Quốc Trung: Histogram
Đinh Huỳnh Nguyên Khang: Statistics
Notes: Hello. We are Group 03. We compare Binary Search, Histogram and Statistics for speech and silence segmentation.

## Slide 2
Shared experiment settings
4 TRAIN WAVs. 4 separate TEST WAVs.
25 ms windows centered on 10 ms decisions.
Normalize STE separately for each WAV.
Merge all silence shorter than 200 ms.
Red: LAB. Blue: predicted boundaries.
F0 is shown as an independent estimate.
Notes: We use four TRAIN WAVs and four separate TEST WAVs. Each 25 ms window is centered on a 10 ms decision cell. We normalize STE per WAV, then fill silence below 200 ms. Red boundaries come from LAB. Blue boundaries come from the algorithm. F0 is an independent estimate.
Sources (reference only): speech_silence/features.py, pipeline.py and demo.py.

## Slide 3
Binary Search
Võ Thanh Quân
TRAIN
Normalize STE
Apply median
LAB frame labels
Keep overlap
Bisect threshold
Score TRAIN
Median = 15. Shared T = 0.0016054242.
TEST
Same TEST features
Median = 15
Fixed threshold
Speech or silence
Fill short silence
Under 200 ms
Notes: On TRAIN, we try six median orders after normalization. LAB timestamps split the frames into silence and speech. We keep only overlapping energy values. Binary Search halves the interval to balance misclassified energy on the two sides. We select the median by extra or missing boundaries, then MAE. This is calibration on TRAIN. The selected median is 15 frames and the shared threshold is about 0.0016. On TEST, we use the same median and threshold, then fill silence shorter than 200 ms.
Sources (reference only): TT1_BinarySearch/algorithm.py, speech_silence/pipeline.py.

## Slide 4
Binary Search: phone_F2
MAE 30 ms
Start matches. End 60 ms late.
Amplitude
STE
Grey: raw STE. Blue: median STE.
T = 0.0016054242
t (s)
0
1
2
3
4
t (s)
0
1
2
3
4
t (s)
0
1
2
3
4
F0 (Hz)
100
200
300
400
Tail median STE remains
above the fixed threshold
Extra: 0. Missed: 0.
Notes: For phone_F2, Start matches. End 60 ms late. MAE is 30 ms, with zero extra or missing boundaries. Tail median STE remains above the fixed threshold. The bottom plot shows F0 and the LAB mean reference.
Sources (reference only): TT1_BinarySearch/ket_qua/phone_F2.png; TT1_BinarySearch/ket_qua/ket_qua.csv. LAB start/end: 1.02 / 4.04 s. Predictions: 1.02 / 4.10 s. The cause is a plot interpretation. LAB mean F0 is not a reference trajectory.

## Slide 5
Binary Search: phone_M2
MAE 0 ms
Start matches. End matches.
Amplitude
STE
Grey: raw STE. Blue: median STE.
T = 0.0016054242
t (s)
0
1
2
t (s)
0
1
2
t (s)
0
1
2
F0 (Hz)
100
200
300
400
Both LAB timestamps match
the detected transitions
Extra: 0. Missed: 0.
Notes: For phone_M2, Start matches. End matches. MAE is 0 ms, with zero extra or missing boundaries. Both LAB timestamps match the detected transitions. The bottom plot shows F0 and the LAB mean reference.
Sources (reference only): TT1_BinarySearch/ket_qua/phone_M2.png; TT1_BinarySearch/ket_qua/ket_qua.csv. LAB start/end: 0.53 / 2.52 s. Predictions: 0.53 / 2.52 s. The cause is a plot interpretation. LAB mean F0 is not a reference trajectory.

## Slide 6
Binary Search: studio_F2
MAE 10 ms
Start 10 ms early. End 10 ms early.
Amplitude
STE
Grey: raw STE. Blue: median STE.
T = 0.0016054242
t (s)
0
1
2
3
t (s)
0
1
2
3
t (s)
0
1
2
3
F0 (Hz)
100
200
300
400
Energy crosses T before
the LAB transitions
Extra: 0. Missed: 0.
Notes: For studio_F2, Start 10 ms early. End 10 ms early. MAE is 10 ms, with zero extra or missing boundaries. Energy crosses T before the LAB transitions. The bottom plot shows F0 and the LAB mean reference.
Sources (reference only): TT1_BinarySearch/ket_qua/studio_F2.png; TT1_BinarySearch/ket_qua/ket_qua.csv. LAB start/end: 0.77 / 2.37 s. Predictions: 0.76 / 2.36 s. The cause is a plot interpretation. LAB mean F0 is not a reference trajectory.

## Slide 7
Binary Search: studio_M2
MAE 5 ms
Start 10 ms late. End matches.
Amplitude
STE
Grey: raw STE. Blue: median STE.
T = 0.0016054242
t (s)
0
1
2
t (s)
0
1
2
t (s)
0
1
2
F0 (Hz)
100
200
300
400
Possible cause: weak
energy near the onset
Extra: 0. Missed: 0.
Notes: For studio_M2, Start 10 ms late. End matches. MAE is 5 ms, with zero extra or missing boundaries. Possible cause: weak energy near the onset. The bottom plot shows F0 and the LAB mean reference.
Sources (reference only): TT1_BinarySearch/ket_qua/studio_M2.png; TT1_BinarySearch/ket_qua/ket_qua.csv. LAB start/end: 0.45 / 1.93 s. Predictions: 0.46 / 1.93 s. The cause is a plot interpretation. LAB mean F0 is not a reference trajectory.

## Slide 8
Histogram
Vương Quốc Trung
TRAIN
TRAIN histograms
128 bins
Try W candidates
Eight values
Score TRAIN boundaries
Errors, then MAE
Selected W = 30. Smooth over 3 bins.
TEST
TEST histogram
Normalized STE
First two peaks
Adaptive threshold
Classify and merge
Silence under 200 ms
Notes: We build 128-bin histograms and smooth the counts over three bins. TRAIN selects W from eight candidates using boundary errors, then MAE. The selected W is 30. For each TEST recording, we choose the first two local peaks along the energy axis. We combine their locations with more weight on the first peak. The threshold therefore adapts to each WAV. If fewer than two peaks exist, we use the mean STE of that WAV. After classification, we fill silence below 200 ms.
Sources (reference only): TT2_Histogram/algorithm.py, speech_silence/pipeline.py.

## Slide 9
Histogram: phone_F2
MAE 10 ms
Start 10 ms late. End 10 ms early.
Amplitude
STE
Normalized STE
T = 0.0054183468
t (s)
0
1
2
3
4
t (s)
0
1
2
3
4
t (s)
0
1
2
3
4
F0 (Hz)
100
200
300
400
Possible cause: weak
energy near the boundaries
Extra: 0. Missed: 0.
Notes: For phone_F2, Start 10 ms late. End 10 ms early. MAE is 10 ms, with zero extra or missing boundaries. Possible cause: weak energy near the boundaries. The bottom plot shows F0 and the LAB mean reference.
Sources (reference only): TT2_Histogram/ket_qua/phone_F2.png; TT2_Histogram/ket_qua/ket_qua.csv. LAB start/end: 1.02 / 4.04 s. Predictions: 1.03 / 4.03 s. The cause is a plot interpretation. LAB mean F0 is not a reference trajectory.

## Slide 10
Histogram: phone_M2
MAE 5 ms
Start matches. End 10 ms early.
Amplitude
STE
Normalized STE
T = 0.0061743952
t (s)
0
1
2
t (s)
0
1
2
t (s)
0
1
2
F0 (Hz)
100
200
300
400
Possible cause: weak
energy near the boundaries
Extra: 0. Missed: 0.
Notes: For phone_M2, Start matches. End 10 ms early. MAE is 5 ms, with zero extra or missing boundaries. Possible cause: weak energy near the boundaries. The bottom plot shows F0 and the LAB mean reference.
Sources (reference only): TT2_Histogram/ket_qua/phone_M2.png; TT2_Histogram/ket_qua/ket_qua.csv. LAB start/end: 0.53 / 2.52 s. Predictions: 0.53 / 2.51 s. The cause is a plot interpretation. LAB mean F0 is not a reference trajectory.

## Slide 11
Histogram: studio_F2
MAE 15 ms
Start 10 ms early. End 20 ms early.
Amplitude
STE
Normalized STE
T = 0.0061743952
t (s)
0
1
2
3
t (s)
0
1
2
3
t (s)
0
1
2
3
F0 (Hz)
100
200
300
400
Onset window includes speech.
Tail energy falls below T.
Extra: 0. Missed: 0.
Notes: For studio_F2, Start 10 ms early. End 20 ms early. MAE is 15 ms, with zero extra or missing boundaries. Onset window includes speech. Tail energy falls below T.. The bottom plot shows F0 and the LAB mean reference.
Sources (reference only): TT2_Histogram/ket_qua/studio_F2.png; TT2_Histogram/ket_qua/ket_qua.csv. LAB start/end: 0.77 / 2.37 s. Predictions: 0.76 / 2.35 s. The cause is a plot interpretation. LAB mean F0 is not a reference trajectory.

## Slide 12
Histogram: studio_M2
MAE 15 ms
Start 20 ms late. End 10 ms early.
Amplitude
STE
Normalized STE
T = 0.0049143145
t (s)
0
1
2
t (s)
0
1
2
t (s)
0
1
2
F0 (Hz)
100
200
300
400
Possible cause: weak
energy near the boundaries
Extra: 0. Missed: 0.
Notes: For studio_M2, Start 20 ms late. End 10 ms early. MAE is 15 ms, with zero extra or missing boundaries. Possible cause: weak energy near the boundaries. The bottom plot shows F0 and the LAB mean reference.
Sources (reference only): TT2_Histogram/ket_qua/studio_M2.png; TT2_Histogram/ket_qua/ket_qua.csv. LAB start/end: 0.45 / 1.93 s. Predictions: 0.47 / 1.92 s. The cause is a plot interpretation. LAB mean F0 is not a reference trajectory.

## Slide 13
Gaussian Statistics
Đinh Huỳnh Nguyên Khang
TRAIN
TRAIN STE
Normalize each WAV
LAB classes
Silence and speech
Mean and std
Gaussian crossing
503 silence, 794 speech. T = 0.0027634166.
TEST
Normalized TEST STE
Same 25 ms windows
Fixed TEST threshold
Shared across WAVs
Classify and merge
Silence under 200 ms
Notes: Statistics uses labeled normalized STE from all four TRAIN recordings. LAB labels give 503 silence frames and 794 speech frames. We calculate each class mean and standard deviation, then choose a Gaussian crossing between the class means. The learned threshold is about 0.00276. We keep it fixed for every TEST WAV. This method uses unfiltered normalized STE. After classification, we fill silence shorter than 200 ms.
Sources (reference only): TT3_Statistics/algorithm.py, TT3_Statistics/ket_qua/tham_so_huan_luyen.json.

## Slide 14
Statistics: phone_F2
MAE 5 ms
Start matches. End 10 ms late.
Amplitude
STE
Normalized STE
T = 0.0027634166
t (s)
0
1
2
3
4
t (s)
0
1
2
3
4
t (s)
0
1
2
3
4
F0 (Hz)
100
200
300
400
Tail STE remains above
the shared threshold
Extra: 0. Missed: 0.
Notes: For phone_F2, Start matches. End 10 ms late. MAE is 5 ms, with zero extra or missing boundaries. Tail STE remains above the shared threshold. The bottom plot shows F0 and the LAB mean reference.
Sources (reference only): TT3_Statistics/ket_qua/phone_F2.png; TT3_Statistics/ket_qua/ket_qua.csv. LAB start/end: 1.02 / 4.04 s. Predictions: 1.02 / 4.05 s. The cause is a plot interpretation. LAB mean F0 is not a reference trajectory.

## Slide 15
Statistics: phone_M2
MAE 5 ms
Start matches. End 10 ms early.
Amplitude
STE
Normalized STE
T = 0.0027634166
t (s)
0
1
2
t (s)
0
1
2
t (s)
0
1
2
F0 (Hz)
100
200
300
400
Possible cause: weak
energy near the boundaries
Extra: 0. Missed: 0.
Notes: For phone_M2, Start matches. End 10 ms early. MAE is 5 ms, with zero extra or missing boundaries. Possible cause: weak energy near the boundaries. The bottom plot shows F0 and the LAB mean reference.
Sources (reference only): TT3_Statistics/ket_qua/phone_M2.png; TT3_Statistics/ket_qua/ket_qua.csv. LAB start/end: 0.53 / 2.52 s. Predictions: 0.53 / 2.51 s. The cause is a plot interpretation. LAB mean F0 is not a reference trajectory.

## Slide 16
Statistics: studio_F2
MAE 15 ms
Start 10 ms early. End 20 ms early.
Amplitude
STE
Normalized STE
T = 0.0027634166
t (s)
0
1
2
3
t (s)
0
1
2
3
t (s)
0
1
2
3
F0 (Hz)
100
200
300
400
Onset window includes speech.
Tail energy falls below T.
Extra: 0. Missed: 0.
Notes: For studio_F2, Start 10 ms early. End 20 ms early. MAE is 15 ms, with zero extra or missing boundaries. Onset window includes speech. Tail energy falls below T.. The bottom plot shows F0 and the LAB mean reference.
Sources (reference only): TT3_Statistics/ket_qua/studio_F2.png; TT3_Statistics/ket_qua/ket_qua.csv. LAB start/end: 0.77 / 2.37 s. Predictions: 0.76 / 2.35 s. The cause is a plot interpretation. LAB mean F0 is not a reference trajectory.

## Slide 17
Statistics: studio_M2
MAE 10 ms
Start 10 ms late. End 10 ms early.
Amplitude
STE
Normalized STE
T = 0.0027634166
t (s)
0
1
2
t (s)
0
1
2
t (s)
0
1
2
F0 (Hz)
100
200
300
400
Possible cause: weak
energy near the boundaries
Extra: 0. Missed: 0.
Notes: For studio_M2, Start 10 ms late. End 10 ms early. MAE is 10 ms, with zero extra or missing boundaries. Possible cause: weak energy near the boundaries. The bottom plot shows F0 and the LAB mean reference.
Sources (reference only): TT3_Statistics/ket_qua/studio_M2.png; TT3_Statistics/ket_qua/ket_qua.csv. LAB start/end: 0.45 / 1.93 s. Predictions: 0.46 / 1.92 s. The cause is a plot interpretation. LAB mean F0 is not a reference trajectory.

## Slide 18
Statistics has the lowest mean TEST MAE (ms)
TEST file | Binary | Histogram | Statistics
phone_F2 | 30 | 10 | 5
phone_M2 | 0 | 5 | 5
studio_F2 | 10 | 15 | 15
studio_M2 | 5 | 15 | 10
Mean | 11.25 | 11.25 | 8.75
Notes: On these four TEST WAVs, Binary Search and Histogram both average 11.25 ms. Statistics averages 8.75 ms, the lowest in our comparison. All three methods match eight reference boundaries with zero extra or missing boundaries. The mean row averages the four files. These results apply to this TEST set.
Sources (reference only): the three TT*/ket_qua/ket_qua.csv and tong_hop.csv files.

## Slide 19
Thank you
Group 03
Võ Thanh Quân
Vương Quốc Trung
Đinh Huỳnh Nguyên Khang
Notes: Thank you for listening.